## Slide 1: Nanopore Sequencing – Data analysis practical session
Alba Sanchis-Juan & Nick Gleadall
Ouwehand Research group

## Slide 2: Aims
Overall: How to take Oxford Nanopore Technology (ONT) data from raw signal to called variants
In this part of the session:
  Learn about data format
  Basecalling
  Basic sequence QC

## Slide 3: Starting point
DNA
Sequence
Library Prep
Raw Data

## Slide 4: Raw reads
All data is written to a run specific directory
$cd ~/data/nanopore_example_run/
$ls reads/
You will see two directories ( 0/ and 1/)
  ONT machines write reads in batches (here batch size = 4,000)
  This is to keep the number of files in each directory reasonable for the computers filesystem
  $ls reads/0/

## Slide 5: FAST5 files
Nanopore writes read data to a file format they call FAST5
FAST5 is in actual fact a HDF5 file
These are compressed binary files which store data in a structured way
This allows for random access to subsets of the data
This is where electronic signal data is storred

## Slide 6: FAST5 files
Lets look at a FAST5 structure (using h5ls)
  $h5ls reads/0/GXB01206_20180518_FAH88225_GA50000_sequencing_run_CD3_92236_read_10011_ch_258_strand.fast5
  This shows the top level data keys, lets look recursively through the file to see the subkeys
  $h5ls -r reads/0/GXB01206_20180518_FAH88225_GA50000_sequencing_run_CD3_92236_read_10011_ch_258_strand.fast5
We can also dump the entire contents of a FAST5
  $h5dump reads/0/GXB01206_20180518_FAH88225_GA50000_sequencing_run_CD3_92236_read_10011_ch_258_strand.fast5 | less
  (HINT: press q to exit less)

## Slide 7: Basecalling
This is the process of translating raw electrical signal from an ONT sequencer to DNA sequence
Critical step in data analysis – it is can make data good or bad
Many basecaller’s are out there but we will use a ALBACORE v2.3.3 one of ONT’s in-house basecallers
It is important to know which flow cell and library kit were used. To see all combinations run:
  $read_fast5_basecaller.py –l
Lets basecall
  $mkdir basecalled_reads
  $read_fast5_basecaller.py --flowcell FLO-MIN106 --kit SQK-PCS108 --input reads/ --recursive --worker_threads 4 --save_path basecalled_reads/

## Slide 8: Basecallers – Assembly Identity
Assembly identity (%)
We don’t care about read identity if overall assembly identity is good

## Slide 9: Basecallers – Assembly length bias
Assembly Length / Reference Length
This lets us see if an assembler is prone to reference insertions/deletions

## Slide 10: Recommended workflows
GridION
PromethION
Onboard GPU Basecalling using latest Guppy
Transfer data to analysis computer
MinION
Transfer data to analysis computer
Basecall using latest Albacore or Chiron 0.3

## Slide 11: Basecalling results
Lets take a look inside the new basecalled_reads directory
  $ls basecalled_reads
Important directory: workspace/
  $ls basecalled_reads/workspace/
  Contains pass/ and fail/ directories. These contain standard fastq seuqence files.
  pass/ contains reads in fastq useable in further analysis.
Important file: sequencing_summary.txt
  This file can be used to plot basic run QC statistics (rather than digging through fast5 files)

## Slide 12: Plotting basic sequence run QC
Much easier to process this data in R
Open RStudio and load the following script:
  ~/data/nanopore_example_run/scripts/basic_sequence_qc.r

## Slide 13: Plotting basic sequence run QC
Much easier to process this data in R
Open RStudio and load the following script:
  /data/nanopore_example_run/scripts/basic_sequence_qc.R
This was a VERY basic overview of plotting
  Check out the poRe library for more advanced plotting
  https://sourceforge.net/p/rpore/wiki/Home/

## Slide 14: Experimental workflow
DNA extraction & Library prep
Sequence
Basecall Fast5’s
Plot basic QC
Alignment
Polish
(Alignment correction)
Call variants and
Analyse data

## Slide 15: List of tools used
  h5ls , h5dump
  ALBACORE v2.3.3
  RStudio & R – any version
  MinMap2 – (BWA for long reads - https://github.com/lh3/minimap2)